Signal processing steps involve detecting and extracting signal packets from OcuSync 1, OcuSync 2, or OcuSync 3, followed by feature extraction and pattern identification & matching.

# Step1:Spectrogram Visualization of Complex Baseband Signal (ocusync1,ocusync2,ocusync3 data)

## 1. Objective
The objective of this work is to read and analyze complex baseband signals stored in .dat binary files using Python. Each file contains complex64 samples representing I/Q data. The goal is to visualize the signal’s frequency content over time by generating a spectrogram, which provides insights into time-frequency behavior — a critical aspect in wireless communications and signal processing.

## 2. Working Principle
The script performs the following operations:
1. Signal Reading:
  1. It reads binary data from a file using numpy.fromfile() as complex64 format (i.e., each sample has a real and imaginary part).
2. Signal Metadata:
  1. It calculates and prints the total number of samples and the signal duration based on the given sampling rate.
3. Spectrogram Generation:
  1. Using matplotlib.pyplot.specgram(), it computes and displays the signal’s spectrogram.
4. User Interaction:
  1. The user is prompted to choose between multiple signal files. Based on the choice, the corresponding spectrogram is plotted.
5. Exit Option:
  1. The script runs in a loop, allowing the user to visualize multiple files until they type 'exit'.

## 💻 Python Code
# Spectrogram Visualization Script for Complex Baseband Signal Data

import numpy as np
import matplotlib.pyplot as plt

def plot_spectrogram(file_path, sampling_rate):
    """
    Reads a binary signal file, computes its spectrogram, and plots it.

    Parameters:
    file_path (str): Path to the .dat file containing complex64 signal data.
    sampling_rate (float): Sampling rate in Hz.
    """
    with open(file_path, "rb") as f:
        signal_data = np.fromfile(f, dtype=np.complex64)

    num_samples = len(signal_data)
    duration = num_samples / sampling_rate # Duration in seconds

    print(f"\nFile: {file_path.split('/')[-1]}")
    print(f"Number of Samples: {num_samples}")
    print(f"Duration: {duration:.6f} seconds")

    plt.close("all")

    plt.figure(figsize=(10, 4))
    plt.specgram(signal_data, Fs=sampling_rate)
    plt.title(f'Spectrogram: {file_path.split("/")[-1]} (Fs = {sampling_rate/1e6:.1f} MHz)',
        fontsize=14, fontweight='bold')
    plt.xlabel("Time (s)")
    plt.ylabel("Frequency (Hz)")
    plt.colorbar(label="Intensity (dB)")
    plt.tight_layout()
    plt.show()

# Predefined file paths and their corresponding sampling rates
sample_files = {
    "1": ("/home/sandeep/OS1_40msps_2.455_GHz__20240522-113218.dat", 40e6),
    "2": ("/home/sandeep/ocusync2_50msps.dat", 50e6),
    "3": ("/home/sandeep/OS3_40msps_2.455_GHz__20240520-145718.dat", 40e6),
}

# User-driven interaction loop
while True:
    file_number = input("\nEnter file number (1, 2, 3) to plot spectrogram, or type 'exit' to quit: ").strip()

    if file_number.lower() == "exit":
        plt.close("all")
        break

    if file_number in sample_files:
        file_path, sampling_rate = sample_files[file_number]
        plot_spectrogram(file_path, sampling_rate)
    else:
        print("Invalid selection. Please enter 1, 2, or 3.")

## 4. Output
When executed, the script will:
- Prompt the user to select one of the listed signal files.
- Display the filename, number of samples, and signal duration in the console.
- Generate a spectrogram plot, showing frequency (Hz) on the y-axis and time (s) on the x-axis.
- The color bar indicates signal intensity (in dB), helping identify active signal regions or modulation structures.
Example Console Output:
Enter file number (1, 2, 3) to plot spectrogram, or type 'exit' to quit: 1

File: Ocusyn1_40msps.dat
Number of Samples: 4000000
Duration: 0.100000 seconds

File: Ocusync2_50msps.dat
Number of Samples: 25000000
Duration: 0.500000 seconds

File: Ocusync3_40msps.dat
Number of Samples: 4000000
Duration: 0.100000 seconds

Example Plot:
A time-frequency spectrogram with color-coded energy levels of the signal across time and frequency.

# Step2:Power Spectral Density Analysis Using Welch’s Method

## 1. Working
This Python script is designed to compute and display the Power Spectral Density (PSD) of complex signal data. The signal data is stored in binary .dat files and consists of complex64 samples. The analysis is performed using Welch’s method, which is a robust technique for estimating the PSD by dividing the signal into overlapping segments and averaging their periodograms. This reduces variance in the estimate.
### Step-by-step Breakdown:
1. File Selection:
  1. The user is prompted to enter a file number (1, 2, or 3), each linked to a different signal file and sampling rate.
2. Signal Loading:
  1. The selected file is read using NumPy’s fromfile() with a complex64 data type.
3. Windowing:
  1. A Hamming window is applied to the signal to reduce spectral leakage.
4. PSD Computation (Welch's method):
  1. scipy.signal.welch() is used to compute the PSD.
  2. The result is then shifted using FFT shift so that the frequency spectrum is centered at 0 Hz (ideal for baseband signals).

## 💻 Python Code
import numpy as np
import matplotlib.pyplot as plt
from scipy.signal import welch, hamming

def compute_psd(signal_data, fs=sampling_rate, nfft_welch=2048):
    """
    Computes and plots the Power Spectral Density (PSD) using Welch's method.

    Parameters:
    signal_data (numpy array): Complex signal data.
    fs (float): Sampling frequency in Hz.
    nfft_welch (int): Number of FFT points for Welch's method.
    """
    if len(signal_data) < nfft_welch:
        print("Insufficient data length for Welch's method")
        return

    window = hamming(len(signal_data))
    data_windowed = signal_data * window

    f, Pxx_den = welch(data_windowed, fs, nperseg=nfft_welch, return_onesided=False)
    Pxx_den_shifted = np.fft.fftshift(Pxx_den)
    f_shifted = np.fft.fftshift(f)

    mean_psd_value = np.mean(Pxx_den_shifted)
    print(f"Mean PSD Value: {mean_psd_value:.2e} V^2/Hz")
    '''
    plt.figure(figsize=(10, 4))
    plt.semilogy(f_shifted / 1e6, Pxx_den_shifted)
    plt.axhline(1.1 * mean_psd_value, color='r', linestyle='--', label="Mean PSD")
    plt.xlabel("Frequency [MHz]")
    plt.ylabel("PSD [V**2/Hz]")
    plt.title("Power Spectral Density (PSD)")
    plt.legend()
    plt.show()
    '''
file_number = input("\nEnter file number (1, 2, 3) to plot PSD, or type 'exit' to quit: ").strip()

if file_number.lower() == "exit":
    plt.close("all") # Close all plots before exiting
else:
    if file_number in sample_files:
        file_path, sampling_rate = sample_files[file_number]

        # Read the signal data
        with open(file_path, "rb") as f:
        signal_data = np.fromfile(f, dtype=np.complex64)

        plt.close("all") # Close previous plot before opening a new one
        compute_psd(signal_data, sampling_rate) # Compute and plot PSD for the selected file
    else:
        print("Invalid selection. Please enter 1, 2, or 3.")

## 3. Output
When the user selects a valid signal file, the output might look like this:
Mean PSD Value: 3.90e-09 V^2/Hz for ocusync1 data
Mean PSD Value: 1.39e-12 V^2/Hz for ocusync2 data
Mean PSD Value: 4.70e-09 V^2/Hz for ocusync3 data
This represents the average power density across the spectrum, useful for estimating the noise floor or for normalizing signal strength.

# Step3:Frequency Spectrum Analysis Using FFT

## 1. Working
This script performs frequency domain analysis of a complex signal using the Fast Fourier Transform (FFT). It allows a user to select a binary file containing complex64 signal samples and then computes and plots its frequency spectrum.
### Key Steps:
1. User Selection:
  1. User selects from three predefined .dat files that represent captured RF signal data.
2. Signal Loading:
  1. The selected binary file is read into a NumPy array as complex64 data.
3. FFT Computation:
  1. FFT is applied to transform the signal from time domain to frequency domain.
  2. The result is shifted so that zero frequency appears in the center of the plot using fftshift.
4. Frequency Axis Generation:
  1. Corresponding frequency bins are calculated using fftfreq and also shifted to align with the FFT output.
5. Plotting (Optional):
  1. The magnitude spectrum is plotted versus frequency in MHz.

## 💻 Python Code
import numpy as np
import matplotlib.pyplot as plt

# Predefined sample files with corresponding sampling rates

def plot_frequency_spectrum(signal_data, sampling_rate):
    """
    Computes and plots the frequency spectrum of the input signal using FFT.

    Parameters:
    - signal_data: Input signal data (numpy array)
    - sampling_rate: The sampling rate of the signal (Hz)
    """
    n = len(signal_data)
    fft_data = np.fft.fft(signal_data)
    fft_data_shifted = np.fft.fftshift(fft_data)
    frequencies = np.fft.fftshift(np.fft.fftfreq(n, 1 / sampling_rate))

    '''
    # Plot the magnitude of the shifted FFT
    plt.figure(figsize=(10, 4))
    plt.plot(frequencies / 1e6, np.abs(fft_data_shifted)) # Convert Hz to MHz
    plt.title('Frequency Spectrum of the Signal')
    plt.xlabel('Frequency (MHz)')
    plt.ylabel('Magnitude')
    plt.grid(True)
    plt.tight_layout()
    plt.show()
    '''

# User input section
file_number = input("\nEnter file number (1, 2, 3) to analyze, or type 'exit' to quit: ").strip()

if file_number.lower() == "exit":
    plt.close("all")
else:
    if file_number in sample_files:
        file_path, sampling_rate = sample_files[file_number]

        # Load the signal data
        with open(file_path, "rb") as f:
        signal_data = np.fromfile(f, dtype=np.complex64)

        plt.close("all")
        plot_frequency_spectrum(signal_data, sampling_rate)
    else:
        print("Invalid selection. Please enter 1, 2, or 3.")

# Step4:Bandpass Filter and Energy-Based signal Packet(burst) Detection in Complex Signals

## 1. Objective
To detect signal packets from raw complex I/Q samples using a bandpass filter followed by an energy-based packet detection algorithm.

## 2. Working Procedure
### Step 1: File Selection
- The user selects one of three .dat files.
- Each file has its associated sampling rate and preferred frequency band (cutoff values).
### Step 2: Read Signal Data
The selected binary .dat file is read using numpy.fromfile() with complex64 data type.
### Step 3: Apply Bandpass Filter
- A 4th order Butterworth filter is applied between user-specified low and high cutoff frequencies.
- This isolates the signal components in the desired frequency band and removes out-of-band noise.
### Step 4: Compute Energy Profile
- Energy is calculated using a sliding window approach (|x|^2 with convolution).
- The size of the sliding window is based on a time duration (window_ms) in milliseconds.
### Step 5: Thresholding
- The average energy is calculated and used as a noise baseline.
- A threshold is applied using a scalar multiplier (threshold_factor) to identify high-energy regions.
### Step 6: Detect Packet Regions
- Continuous high-energy segments are extracted as potential packets.
- Segments shorter than a defined minimum duration (640 µs) are filtered out.
### Step 7: Output Valid Packets
- Valid packets are printed with start time, end time, and duration.
- Optional plots (commented out) include energy profiles and spectrograms of detected packets.

## 💻 Python Code
import numpy as np
import matplotlib.pyplot as plt
from scipy.signal import butter, filtfilt

def bandpass_filter(data, sampling_rate, low_cutoff, high_cutoff, order=4):
    """
    Apply a bandpass filter to isolate the desired frequency range.
    """
    nyquist = sampling_rate / 2.0
    low = low_cutoff / nyquist
    high = high_cutoff / nyquist
    b, a = butter(order, [low, high], btype='band')
    return filtfilt(b, a, data)

def detect_packets_energy(data, sampling_rate, window_ms, threshold_factor):
    """
    Detect signal packets based on energy accumulation.
    """
    window_samples = int((window_ms / 1000) * sampling_rate)
    energy_profile = np.convolve(np.abs(data)**2, np.ones(window_samples), mode='same')

    noise_level = np.mean(energy_profile) # Baseline noise level
    threshold = threshold_factor * noise_level

    detected = energy_profile > threshold
    packets = []
    start = None

    for i, is_high in enumerate(detected):
        if is_high and start is None:
        start = i
        elif not is_high and start is not None:
        packets.append((start, i))
        start = None

    if start is not None:
        packets.append((start, len(detected)))

    return packets, energy_profile, threshold

# Define cutoff frequencies only (no repetition of sample_files)
cutoff_frequencies = {
    "1": (4.5e6, 19.9e6),
    "2": (6e6, 24e6),
    "3": (5e6, 14e6)
}

selection = input("\nPress 1 for index 1, 2 for index 2, or 3 for index 3: ").strip()

if selection in sample_files:
    file_path, sampling_rate = sample_files[selection] # Using sample_files from previous cell
    low_cutoff, high_cutoff = cutoff_frequencies[selection]

    # Read the signal data
    with open(file_path, "rb") as f:
        signal_data = np.fromfile(f, dtype=np.complex64)

    # Step 1: Apply Bandpass Filter
    filtered_data = bandpass_filter(signal_data, sampling_rate, low_cutoff, high_cutoff)

    # Step 2: Detect Signal Packets
    window_ms = 0.108 # Window size in milliseconds
    threshold_factor = 0.9 # Threshold multiplier
    packets, energy_profile, threshold = detect_packets_energy(filtered_data, sampling_rate, window_ms, threshold_factor)

    # Step 3: Filter Out Short Packets
    valid_duration_threshold = 640e-6 # 600 microseconds
    valid_packets = [
        (start_idx, end_idx) for start_idx, end_idx in packets
        if (end_idx - start_idx) / sampling_rate >= valid_duration_threshold
    ]

    # Step 4: Plot Energy Profile
    '''
    plt.figure(figsize=(12, 6))
    plt.plot(energy_profile, label="Energy Profile", color="blue")
    plt.axhline(y=threshold, color="red", linestyle="--", label="Threshold")
    plt.title(f"Energy Profile with Detected Signal Packets (Index {selection})")
    plt.xlabel("Sample Index")
    plt.ylabel("Energy")
    plt.legend()
    plt.grid()
    plt.show()
    '''
    # Step 5: Plot Spectrograms for Detected Packets
    print(f"Number of detected packets: {len(valid_packets)}")
    for idx, (start_idx, end_idx) in enumerate(valid_packets, start=1):
        start_time = start_idx / sampling_rate
        end_time = end_idx / sampling_rate
        print(f"Packet {idx}: Start Time = {start_time:.6f} s, End Time = {end_time:.6f} s, Duration = {(end_time - start_time) * 1000:.3f} ms")

        packet_data = signal_data[start_idx:end_idx]
        '''
        plt.figure(figsize=(10, 4))
        plt.specgram(packet_data, NFFT=256, Fs=sampling_rate, noverlap=128, cmap='viridis', scale='dB')
        plt.title(f"Spectrogram of Detected Packet {idx}")
        plt.xlabel("Time [s]")
        plt.ylabel("Frequency [Hz]")
        plt.colorbar(label="Power/Frequency [dB]")
        plt.show()
        '''
else:
    print("Invalid selection. Please enter 1, 2, or 3.")

## 4. Output
For ocusync1 data:
Press 1 for index 1, 2 for index 2, or 3 for index 3: 1
Number of detected packets: 19
Packet 1: Start Time = 0.007507 s, End Time = 0.009259 s, Duration = 1.752 ms Packet 2: Start Time = 0.011286 s, End Time = 0.013259 s, Duration = 1.973 ms Packet 3: Start Time = 0.014191 s, End Time = 0.019242 s, Duration = 5.051 ms Packet 4: Start Time = 0.020191 s, End Time = 0.023260 s, Duration = 3.069 ms Packet 5: Start Time = 0.025312 s, End Time = 0.029234 s, Duration = 3.922 ms Packet 6: Start Time = 0.030192 s, End Time = 0.033237 s, Duration = 3.044 ms Packet 7: Start Time = 0.034192 s, End Time = 0.039257 s, Duration = 5.065 ms Packet 8: Start Time = 0.040193 s, End Time = 0.043231 s, Duration = 3.037 ms Packet 9: Start Time = 0.044193 s, End Time = 0.049249 s, Duration = 5.056 ms Packet 10: Start Time = 0.051294 s, End Time = 0.053248 s, Duration = 1.954 ms Packet 11: Start Time = 0.054195 s, End Time = 0.059243 s, Duration = 5.048 ms Packet 12: Start Time = 0.060195 s, End Time = 0.063256 s, Duration = 3.061 ms Packet 13: Start Time = 0.065298 s, End Time = 0.069245 s, Duration = 3.947 ms Packet 14: Start Time = 0.070195 s, End Time = 0.073239 s, Duration = 3.043 ms Packet 15: Start Time = 0.074195 s, End Time = 0.079259 s, Duration = 5.064 ms Packet 16: Start Time = 0.080195 s, End Time = 0.083244 s, Duration = 3.048 ms Packet 17: Start Time = 0.084195 s, End Time = 0.089238 s, Duration = 5.043 ms Packet 18: Start Time = 0.091307 s, End Time = 0.093241 s, Duration = 1.934 ms Packet 19: Start Time = 0.094195 s, End Time = 0.099245 s, Duration = 5.050 ms

for ocusync2 data:

Number of detected packets: 101
Packet 1: Start Time = 0.000020 s, End Time = 0.004107 s, Duration = 4.087 ms
Packet 2: Start Time = 0.006160 s, End Time = 0.008107 s, Duration = 1.947 ms
Packet 3: Start Time = 0.009147 s, End Time = 0.014108 s, Duration = 4.960 ms
Packet 4: Start Time = 0.015146 s, End Time = 0.018109 s, Duration = 2.963 ms
Packet 5: Start Time = 0.019143 s, End Time = 0.024110 s, Duration = 4.966 ms
Packet 6: Start Time = 0.026158 s, End Time = 0.028110 s, Duration = 1.952 ms
Packet 7: Start Time = 0.029144 s, End Time = 0.034108 s, Duration = 4.964 ms
Packet 8: Start Time = 0.036159 s, End Time = 0.038108 s, Duration = 1.949 ms
Packet 9: Start Time = 0.039148 s, End Time = 0.044107 s, Duration = 4.959 ms
Packet 10: Start Time = 0.045149 s, End Time = 0.047107 s, Duration = 1.959 ms
Packet 11: Start Time = 0.049148 s, End Time = 0.054106 s, Duration = 4.957 ms
Packet 12: Start Time = 0.055148 s, End Time = 0.058106 s, Duration = 2.958 ms
Packet 13: Start Time = 0.059149 s, End Time = 0.064105 s, Duration = 4.956 ms
Packet 14: Start Time = 0.065147 s, End Time = 0.068107 s, Duration = 2.960 ms
Packet 15: Start Time = 0.069146 s, End Time = 0.074108 s, Duration = 4.962 ms
Packet 16: Start Time = 0.076156 s, End Time = 0.078109 s, Duration = 1.953 ms
Packet 17: Start Time = 0.079142 s, End Time = 0.084113 s, Duration = 4.971 ms
Packet 18: Start Time = 0.086157 s, End Time = 0.088112 s, Duration = 1.955 ms
Packet 19: Start Time = 0.089141 s, End Time = 0.094111 s, Duration = 4.970 ms
Packet 20: Start Time = 0.095141 s, End Time = 0.098112 s, Duration = 2.971 ms
Packet 21: Start Time = 0.099142 s, End Time = 0.104111 s, Duration = 4.969 ms
Packet 22: Start Time = 0.106157 s, End Time = 0.108109 s, Duration = 1.952 ms
Packet 23: Start Time = 0.109144 s, End Time = 0.114107 s, Duration = 4.963 ms
Packet 24: Start Time = 0.116160 s, End Time = 0.118105 s, Duration = 1.945 ms
...
Packet 98: Start Time = 0.486159 s, End Time = 0.488110 s, Duration = 1.951 ms
Packet 99: Start Time = 0.489145 s, End Time = 0.494111 s, Duration = 4.966 ms
Packet 100: Start Time = 0.495144 s, End Time = 0.498112 s, Duration = 2.968 ms
Packet 101: Start Time = 0.499142 s, End Time = 0.499984 s, Duration = 0.841 ms

for ocusync3 data:
Number of detected packets: 28
Packet 1: Start Time = 0.007767 s, End Time = 0.008875 s, Duration = 1.108 ms
Packet 2: Start Time = 0.010752 s, End Time = 0.012875 s, Duration = 2.124 ms
Packet 3: Start Time = 0.015768 s, End Time = 0.016875 s, Duration = 1.107 ms
Packet 4: Start Time = 0.017768 s, End Time = 0.018874 s, Duration = 1.106 ms
Packet 5: Start Time = 0.020757 s, End Time = 0.022873 s, Duration = 2.116 ms
Packet 6: Start Time = 0.025768 s, End Time = 0.026874 s, Duration = 1.106 ms
Packet 7: Start Time = 0.027769 s, End Time = 0.028872 s, Duration = 1.103 ms
Packet 8: Start Time = 0.030751 s, End Time = 0.032871 s, Duration = 2.121 ms
Packet 9: Start Time = 0.035772 s, End Time = 0.036875 s, Duration = 1.103 ms
Packet 10: Start Time = 0.037769 s, End Time = 0.038871 s, Duration = 1.102 ms
Packet 11: Start Time = 0.040755 s, End Time = 0.042872 s, Duration = 2.116 ms
Packet 12: Start Time = 0.045773 s, End Time = 0.046869 s, Duration = 1.095 ms
Packet 13: Start Time = 0.047773 s, End Time = 0.048869 s, Duration = 1.096 ms
Packet 14: Start Time = 0.051774 s, End Time = 0.052868 s, Duration = 1.094 ms
Packet 15: Start Time = 0.055774 s, End Time = 0.056868 s, Duration = 1.093 ms
Packet 16: Start Time = 0.057775 s, End Time = 0.058869 s, Duration = 1.094 ms
Packet 17: Start Time = 0.060760 s, End Time = 0.062867 s, Duration = 2.106 ms
Packet 18: Start Time = 0.065776 s, End Time = 0.066866 s, Duration = 1.091 ms
Packet 19: Start Time = 0.067776 s, End Time = 0.068866 s, Duration = 1.090 ms
Packet 20: Start Time = 0.071776 s, End Time = 0.072866 s, Duration = 1.090 ms
Packet 21: Start Time = 0.075776 s, End Time = 0.076866 s, Duration = 1.090 ms
Packet 22: Start Time = 0.077776 s, End Time = 0.078867 s, Duration = 1.090 ms
Packet 23: Start Time = 0.080754 s, End Time = 0.082867 s, Duration = 2.113 ms
Packet 24: Start Time = 0.085776 s, End Time = 0.086870 s, Duration = 1.094 ms
Packet 25: Start Time = 0.087772 s, End Time = 0.088867 s, Duration = 1.095 ms
Packet 26: Start Time = 0.090758 s, End Time = 0.092867 s, Duration = 2.108 ms
Packet 27: Start Time = 0.095775 s, End Time = 0.096867 s, Duration = 1.092 ms
Packet 28: Start Time = 0.097775 s, End Time = 0.098868 s, Duration = 1.092 ms
### ✅ Advantages
- Simple & Fast: Easy to implement with low computational cost.
- No Prior Knowledge Needed: Doesn't require a known reference signal.
- Works in Real-Time: Suitable for quick detection in streaming applications.
- Effective in High SNR: Performs well when signals are strong and noise is low.

### 🔋 Limitations of Energy-Based Algorithms
1. 🚫 Poor Noise Robustness
  1. Energy-based detection can be significantly impacted by high noise levels or low signal-to-noise ratios (SNR).
  2. Noise bursts can falsely appear as high-energy regions, leading to false positives.

# Step5: Frequency Offset Estimation and Correction for Drone Signal Packets

## 1. Objective
To estimate and correct the carrier frequency offset in signal packets detected from drone communication recordings, using PSD analysis and frequency domain filtering techniques.

## 2. Working Procedure
### Step 1: Initialize Signal Parameters
- Define file paths and corresponding sampling rates using sample_files.
- Define cutoff_frequencies based on expected signal bands for different drone modes (1, 2, or 3).
### Step 2: User Input Selection
- The user selects a dataset by entering 1, 2, or 3.
- The selection determines the file path, sampling rate, and frequency band of interest.
### Step 3: Load Signal Data
The selected .dat file is read using numpy.fromfile() as complex64 baseband data.
### Step 4: Define Processing Class
- The DroneSignalProcessor class handles:
  - Frequency offset estimation via Power Spectral Density (PSD).
  - Correction using complex exponential modulation.
  - Grouping of consecutive high-energy bins using a utility method.
### Step 5: Estimate Frequency Offset
- For each valid_packet, extract the data segment.
- Apply a Hamming window and compute PSD using the Welch method.
- Inject a DC carrier bias to avoid false detection at zero frequency.
- Detect regions where PSD is significantly above average (potential signal bands).
- Calculate bandwidth, start/end frequencies, and check if they fall within expected range.
### Step 6: Apply Frequency Shift Correction
- If a suitable band is found:
  - Apply complex exponential frequency correction using fshift().
  - Store corrected packets for further analysis or classification.
- If no suitable band is found, the packet is skipped.

## 💻 Python Code
import numpy as np
import matplotlib.pyplot as plt
from scipy.signal import butter, filtfilt, welch, hamming

class DroneSignalProcessor:
    def __init__(self, debug=True):
        self.debug = debug

    @staticmethod
    def fshift(y, offset, Fs):
        """Shift the frequency of the signal."""
        print(f"Signal Length: {len(y)}, Offset: {offset} Hz, Sampling Rate: {Fs} Hz")
        x = np.linspace(0.0, len(y) / Fs, len(y))
        return y * np.exp(x * 2j * np.pi * offset) # Apply frequency shift correction

    def consecutive(self, data, stepsize=1):
        """Group consecutive elements based on a step size."""
        return np.split(data, np.where(np.diff(data) != stepsize)[0] + 1)

    def estimate_offset(self, y, Fs, packet_type="droneid", selection="1"):
        """Estimate the frequency offset in the signal."""
        nfft_welch = 1024 # FFT size for PSD calculation

        if len(y) < nfft_welch:
        return None, False

        # Apply Hamming window
        window = hamming(len(y))
        y = y * window

        # Compute Power Spectral Density (PSD)
        f, Pxx_den = welch(y, Fs, nfft=nfft_welch, return_onesided=False)
        Pxx_den = np.fft.fftshift(Pxx_den)
        f = np.fft.fftshift(f)

        # Add a fake DC carrier to distinguish signal components
        Pxx_den[nfft_welch // 2 - 10:nfft_welch // 2 + 10] = 1.1 * Pxx_den.mean()

        # Identify candidate frequency bands
        candidate_bands = self.consecutive(np.where(Pxx_den > 0.7 * Pxx_den.mean())[0])

        band_found = False
        offset = 0.0

        for band in candidate_bands:
        start = band[0] - nfft_welch / 2
        end = band[-1] - nfft_welch / 2
        bw = (end - start) * (Fs / nfft_welch)
        fend = start * Fs / nfft_welch
        fstart = end * Fs / nfft_welch

        if self.debug:
        print(f"Candidate band fstart: {fstart:.2f}, fend: {fend:.2f}, bw: {bw / 1e6:.2f} MHz")

        if selection == "1" and -19.99e6 <= fstart - 0.5 * bw <= -4.5e6:
        offset = fstart - 0.5 * bw
        band_found = True
        break
        elif selection == "2" and -24e6 <= fstart - 0.5 * bw <= -6e6:
        offset = fstart - 0.5 * bw
        band_found = True
        break
        elif selection == "3" and -13.5e6 <= fstart - 0.5 * bw <= 4.5e6:
        offset = fstart - 0.5 * bw
        band_found = True
        break

        if self.debug:
        print(f"Offset found: {offset / 1000:.2f} kHz")
        return offset, band_found

# Define cutoff frequencies for different selections
cutoff_frequencies = {
    "1": (4.5e6, 19.99e6),
    "2": (6e6, 24e6),
    "3": (5e6, 14e6)
}

# === Simulated definitions for the demo (remove/replace with your actual values) ===
# sample_files and valid_packets should be defined before this cell
# For example:
# sample_files = {
# "1": ("/path/to/file1.dat", 50e6),
# "2": ("/path/to/file2.dat", 50e6),
# "3": ("/path/to/file3.dat", 50e6)
# }
# valid_packets = [(start_idx1, end_idx1), (start_idx2, end_idx2), ...]
# ===================================================================================

# User input for selection
selection = input("\nPress 1 for index 1, 2 for index 2, or 3 for index 3: ").strip()

# List to store corrected packets for later use
corrected_packets = []

# Check if selection exists
if selection in sample_files:
    file_path, sampling_rate = sample_files[selection]
    low_cutoff, high_cutoff = cutoff_frequencies[selection]

    # Read the signal data
    with open(file_path, "rb") as f:
        signal_data = np.fromfile(f, dtype=np.complex64)

    # Process each detected packet
    processor = DroneSignalProcessor(debug=False)
    for idx, (start_idx, end_idx) in enumerate(valid_packets, start=1):
        start_time = start_idx / sampling_rate
        end_time = end_idx / sampling_rate
        duration_ms = (end_time - start_time) * 1000

        print(f"Packet {idx}: Start Time = {start_time:.6f} s, End Time = {end_time:.6f} s, Duration = {duration_ms:.3f} ms")

        # Extract the packet
        packet_data = signal_data[start_idx:end_idx]

        # Estimate frequency offset
        offset, band_found = processor.estimate_offset(packet_data, sampling_rate, packet_type="droneid", selection=selection)

        if band_found:
        print(f"Packet {idx}: Estimated Frequency Offset = {offset / 1000:.2f} kHz")

        # Apply frequency offset correction
        corrected_packet = DroneSignalProcessor.fshift(packet_data, -offset, sampling_rate)

        # Store for later use
        corrected_packets.append(corrected_packet)

        else:
        print(f"Packet {idx}: No suitable band found for offset correction.")
else:
    print("Invalid selection. Please enter 1, 2, or 3.")

## 4. Output
For ocusync1 data:
Packet 1: Estimated Frequency Offset = -12031.25 kHz Signal Length: 70076, Offset: 12031250.0 Hz, Sampling Rate: 40000000.0 Hz
Packet 2: Estimated Frequency Offset = -12070.31 kHz Signal Length: 78903, Offset: 12070312.5 Hz, Sampling Rate: 40000000.0 Hz
Packet 3: Estimated Frequency Offset = -12070.31 kHz Signal Length: 202048, Offset: 12070312.5 Hz, Sampling Rate: 40000000.0 Hz
Packet 4: Estimated Frequency Offset = -12070.31 kHz Signal Length: 122744, Offset: 12070312.5 Hz, Sampling Rate: 40000000.0 Hz
Packet 5: Estimated Frequency Offset = -12109.38 kHz Signal Length: 156891, Offset: 12109375.0 Hz, Sampling Rate: 40000000.0 Hz
Packet 6: Estimated Frequency Offset = -12089.84 kHz Signal Length: 121771, Offset: 12089843.75 Hz, Sampling Rate: 40000000.0 Hz
Packet 7: Estimated Frequency Offset = -12070.31 kHz Signal Length: 202610, Offset: 12070312.5 Hz, Sampling Rate: 40000000.0 Hz
Packet 8: Estimated Frequency Offset = -12128.91 kHz Signal Length: 121498, Offset: 12128906.25 Hz, Sampling Rate: 40000000.0 Hz
Packet 9: Estimated Frequency Offset = -12070.31 kHz Signal Length: 202241, Offset: 12070312.5 Hz, Sampling Rate: 40000000.0 Hz
Packet 10: Estimated Frequency Offset = -12089.84 kHz Signal Length: 78160, Offset: 12089843.75 Hz, Sampling Rate: 40000000.0 Hz
Packet 11: Estimated Frequency Offset = -12109.38 kHz Signal Length: 201921, Offset: 12109375.0 Hz, Sampling Rate: 40000000.0 Hz
Packet 12: Estimated Frequency Offset = -12089.84 kHz Signal Length: 122448, Offset: 12089843.75 Hz, Sampling Rate: 40000000.0 Hz
Packet 13: Estimated Frequency Offset = -12089.84 kHz
...
Packet 18: Estimated Frequency Offset = -12109.38 kHz Signal Length: 77348, Offset: 12109375.0 Hz, Sampling Rate: 40000000.0 Hz
Packet 19: Estimated Frequency Offset = -12089.84 kHz Signal Length: 202002, Offset: 12089843.75 Hz, Sampling Rate: 40000000.0 Hz

for ocusync2 data:

Packet 1: Estimated Frequency Offset = -14965.82 kHz Signal Length: 204369, Offset: 14965820.3125 Hz, Sampling Rate: 50000000.0 Hz
Packet 2: Estimated Frequency Offset = -14965.82 kHz Signal Length: 97369, Offset: 14965820.3125 Hz, Sampling Rate: 50000000.0 Hz
Packet 3: Estimated Frequency Offset = -14965.82 kHz Signal Length: 248021, Offset: 14965820.3125 Hz, Sampling Rate: 50000000.0 Hz
Packet 4: Estimated Frequency Offset = -14965.82 kHz Signal Length: 148175, Offset: 14965820.3125 Hz, Sampling Rate: 50000000.0 Hz
Packet 5: Estimated Frequency Offset = -14965.82 kHz Signal Length: 248306, Offset: 14965820.3125 Hz, Sampling Rate: 50000000.0 Hz
Packet 6: Estimated Frequency Offset = -14965.82 kHz Signal Length: 97583, Offset: 14965820.3125 Hz, Sampling Rate: 50000000.0 Hz
Packet 7: Estimated Frequency Offset = -14965.82 kHz Signal Length: 248215, Offset: 14965820.3125 Hz, Sampling Rate: 50000000.0 Hz
Packet 8: Estimated Frequency Offset = -14965.82 kHz Signal Length: 97432, Offset: 14965820.3125 Hz, Sampling Rate: 50000000.0 Hz
Packet 9: Estimated Frequency Offset = -14965.82 kHz Signal Length: 247938, Offset: 14965820.3125 Hz, Sampling Rate: 50000000.0 Hz
Packet 10: Estimated Frequency Offset = -14965.82 kHz Signal Length: 97940, Offset: 14965820.3125 Hz, Sampling Rate: 50000000.0 Hz
Packet 11: Estimated Frequency Offset = -14965.82 kHz Signal Length: 247870, Offset: 14965820.3125 Hz, Sampling Rate: 50000000.0 Hz
Packet 12: Estimated Frequency Offset = -14965.82 kHz Signal Length: 147900, Offset: 14965820.3125 Hz, Sampling Rate: 50000000.0 Hz
Packet 13: Estimated Frequency Offset = -14965.82 kHz
...
Packet 100: Estimated Frequency Offset = -14965.82 kHz Signal Length: 148425, Offset: 14965820.3125 Hz, Sampling Rate: 50000000.0 Hz
Packet 101: Estimated Frequency Offset = -14965.82 kHz Signal Length: 42058, Offset: 14965820.3125 Hz, Sampling Rate: 50000000.0 Hz

for ocusync3 data:
Packet 1: Estimated Frequency Offset = -4550.78 kHz Signal Length: 44328, Offset: 4550781.25 Hz, Sampling Rate: 40000000.0 Hz
Packet 2: Estimated Frequency Offset = -4531.25 kHz Signal Length: 84954, Offset: 4531250.0 Hz, Sampling Rate: 40000000.0 Hz
Packet 3: Estimated Frequency Offset = -4550.78 kHz Signal Length: 44263, Offset: 4550781.25 Hz, Sampling Rate: 40000000.0 Hz
acket 4: Estimated Frequency Offset = -4550.78 kHz Signal Length: 44243, Offset: 4550781.25 Hz, Sampling Rate: 40000000.0 Hz
Packet 5: Estimated Frequency Offset = -4550.78 kHz Signal Length: 84651, Offset: 4550781.25 Hz, Sampling Rate: 40000000.0 Hz
Packet 6: Estimated Frequency Offset = -4550.78 kHz Signal Length: 44254, Offset: 4550781.25 Hz, Sampling Rate: 40000000.0 Hz
Packet 7: Estimated Frequency Offset = -4531.25 kHz Signal Length: 44120, Offset: 4531250.0 Hz, Sampling Rate: 40000000.0 Hz
Packet 8: Estimated Frequency Offset = -4570.31 kHz Signal Length: 84825, Offset: 4570312.5 Hz, Sampling Rate: 40000000.0 Hz
Packet 9: Estimated Frequency Offset = -4550.78 kHz Signal Length: 44118, Offset: 4550781.25 Hz, Sampling Rate: 40000000.0 Hz
Packet 10: Estimated Frequency Offset = -4550.78 kHz Signal Length: 44097, Offset: 4550781.25 Hz, Sampling Rate: 40000000.0 Hz
Packet 11: Estimated Frequency Offset = -4570.31 kHz Signal Length: 84655, Offset: 4570312.5 Hz, Sampling Rate: 40000000.0 Hz
Packet 12: Estimated Frequency Offset = -4570.31 kHz Signal Length: 43819, Offset: 4570312.5 Hz, Sampling Rate: 40000000.0 Hz
Packet 13: Estimated Frequency Offset = -4550.78 kHz
...
Packet 27: Estimated Frequency Offset = -4570.31 kHz Signal Length: 43695, Offset: 4570312.5 Hz, Sampling Rate: 40000000.0 Hz
Packet 28: Estimated Frequency Offset = -4550.78 kHz Signal Length: 43695, Offset: 4550781.25 Hz, Sampling Rate: 40000000.0 Hz

## 5. Key Features and Benefits
✅ Frequency offset estimation is adaptive to signal strength and bandwidth
✅ Robust against DC bias using fake DC peak injection
✅ Band detection is flexible for different drone signal configurations
✅ Corrected packets are stored for post-processing (e.g., decoding, classification)

Here you go — a complete breakdown with:
1. Working Procedure
2. Full Code
3. Outcome (Result)

## ✅ Working Procedure (Step-by-step)
1. Purpose:
   Analyze and visualize the Power Spectral Density (PSD) of frequency-corrected signal packets using Welch’s method.
2. Steps:
  1. Iterate over each packet in the list of corrected_packets.
  2. Skip any packet shorter than the FFT size (nfft_welch).
  3. Apply a Hamming window to reduce spectral leakage.
  4. Compute the PSD using Welch’s method.
  5. Apply FFT shift for center-aligned frequency display.
  6. Calculate and print the mean PSD value.
  7. (Optional) Plot the PSD using a logarithmic Y-scale for better visibility.

## 🧠 Python Code
import numpy as np
import matplotlib.pyplot as plt
from scipy.signal import welch, hamming

def plot_psd_from_corrected_packets(corrected_packets, sampling_rate, nfft_welch=1024):
    """
    Plots the Power Spectral Density (PSD) of already frequency-corrected packets.

    Parameters:
        corrected_packets (list of np.ndarray): List of corrected signal packets.
        sampling_rate (float): Sampling frequency in Hz.
        nfft_welch (int): Number of FFT points for Welch’s method (default: 1024).
    """
    for idx, corrected_packet in enumerate(corrected_packets, start=1):
        signal_len = len(corrected_packet)

        if signal_len < nfft_welch:
        print(f"Packet {idx}: Skipped (too short for Welch's method)")
        continue

        # Apply Hamming window
        window = hamming(signal_len)
        data_windowed = corrected_packet * window

        # Compute PSD using Welch's method
        f, Pxx_den = welch(data_windowed, sampling_rate, nperseg=nfft_welch, return_onesided=False)

        # Shift for symmetrical spectrum
        f_shifted = np.fft.fftshift(f)
        Pxx_den_shifted = np.fft.fftshift(Pxx_den)

        # Mean PSD
        mean_psd_value = np.mean(Pxx_den_shifted)
        print(f"Mean PSD Value for Packet {idx}: {mean_psd_value:.2e} V²/Hz")
        '''
        # Plot
        plt.figure(figsize=(10, 4))
        plt.semilogy(f_shifted / 1e6, Pxx_den_shifted)
        plt.axhline(1.1 * mean_psd_value, color='r', linestyle='--', label="1.1 × Mean PSD")
        plt.xlabel("Frequency [MHz]")
        plt.ylabel("PSD [V²/Hz]")
        plt.title(f"Power Spectral Density (Corrected Packet {idx})")
        plt.grid(True, linestyle='--', alpha=0.5)
        plt.legend()
        plt.tight_layout()
        plt.show()
        '''
plot_psd_from_corrected_packets(corrected_packets, sampling_rate)

## 📊 Outcome
- For each frequency-corrected packet:
  - Prints the mean PSD value in V²/Hz.
Mean PSD Value for Packet 1: 5.18e-09 V²/Hz
Mean PSD Value for Packet 2: 5.12e-09 V²/Hz
Mean PSD Value for Packet 3: 3.96e-09 V²/Hz
Mean PSD Value for Packet 4: 5.20e-09 V²/Hz
Mean PSD Value for Packet 5: 3.69e-09 V²/Hz
Mean PSD Value for Packet 6: 4.09e-09 V²/Hz
Mean PSD Value for Packet 7: 4.17e-09 V²/Hz
Mean PSD Value for Packet 8: 3.55e-09 V²/Hz
Mean PSD Value for Packet 9: 5.02e-09 V²/Hz
Mean PSD Value for Packet 10: 4.55e-09 V²/Hz
Mean PSD Value for Packet 11: 4.20e-09 V²/Hz
Mean PSD Value for Packet 12: 4.79e-09 V²/Hz
Mean PSD Value for Packet 13: 4.31e-09 V²/Hz
Mean PSD Value for Packet 14: 4.25e-09 V²/Hz
Mean PSD Value for Packet 15: 4.28e-09 V²/Hz
Mean PSD Value for Packet 16: 4.18e-09 V²/Hz
Mean PSD Value for Packet 17: 4.66e-09 V²/Hz
Mean PSD Value for Packet 18: 4.09e-09 V²/Hz
Mean PSD Value for Packet 19: 4.24e-09 V²/Hz

for ocusync2 data:
Mean PSD Value for Packet 1: 1.82e-12 V²/Hz
Mean PSD Value for Packet 2: 1.83e-12 V²/Hz
Mean PSD Value for Packet 3: 1.82e-12 V²/Hz
Mean PSD Value for Packet 4: 1.83e-12 V²/Hz
Mean PSD Value for Packet 5: 1.85e-12 V²/Hz
Mean PSD Value for Packet 6: 1.87e-12 V²/Hz
Mean PSD Value for Packet 7: 1.84e-12 V²/Hz
Mean PSD Value for Packet 8: 1.81e-12 V²/Hz
Mean PSD Value for Packet 9: 1.78e-12 V²/Hz
Mean PSD Value for Packet 10: 1.78e-12 V²/Hz
Mean PSD Value for Packet 11: 1.78e-12 V²/Hz
Mean PSD Value for Packet 12: 1.76e-12 V²/Hz
Mean PSD Value for Packet 13: 1.75e-12 V²/Hz
Mean PSD Value for Packet 14: 1.77e-12 V²/Hz
Mean PSD Value for Packet 15: 1.82e-12 V²/Hz
Mean PSD Value for Packet 16: 1.87e-12 V²/Hz
Mean PSD Value for Packet 17: 1.88e-12 V²/Hz
Mean PSD Value for Packet 18: 1.92e-12 V²/Hz
Mean PSD Value for Packet 19: 1.92e-12 V²/Hz
Mean PSD Value for Packet 20: 1.91e-12 V²/Hz
Mean PSD Value for Packet 21: 1.89e-12 V²/Hz
Mean PSD Value for Packet 22: 1.88e-12 V²/Hz
Mean PSD Value for Packet 23: 1.83e-12 V²/Hz
Mean PSD Value for Packet 24: 1.81e-12 V²/Hz
Mean PSD Value for Packet 25: 1.80e-12 V²/Hz
...
Mean PSD Value for Packet 98: 1.86e-12 V²/Hz
Mean PSD Value for Packet 99: 1.87e-12 V²/Hz
Mean PSD Value for Packet 100: 1.88e-12 V²/Hz
Mean PSD Value for Packet 101: 1.90e-12 V²/Hz

for ocusync3 data:
Mean PSD Value for Packet 1: 1.11e-08 V²/Hz
Mean PSD Value for Packet 2: 1.10e-08 V²/Hz
Mean PSD Value for Packet 3: 1.08e-08 V²/Hz
Mean PSD Value for Packet 4: 1.08e-08 V²/Hz
Mean PSD Value for Packet 5: 1.02e-08 V²/Hz
Mean PSD Value for Packet 6: 1.02e-08 V²/Hz
Mean PSD Value for Packet 7: 1.02e-08 V²/Hz
Mean PSD Value for Packet 8: 1.00e-08 V²/Hz
Mean PSD Value for Packet 9: 9.86e-09 V²/Hz
Mean PSD Value for Packet 10: 9.85e-09 V²/Hz
Mean PSD Value for Packet 11: 9.37e-09 V²/Hz
Mean PSD Value for Packet 12: 9.46e-09 V²/Hz
Mean PSD Value for Packet 13: 9.45e-09 V²/Hz
Mean PSD Value for Packet 14: 9.28e-09 V²/Hz
Mean PSD Value for Packet 15: 9.07e-09 V²/Hz
Mean PSD Value for Packet 16: 9.08e-09 V²/Hz
Mean PSD Value for Packet 17: 8.67e-09 V²/Hz
Mean PSD Value for Packet 18: 8.83e-09 V²/Hz
Mean PSD Value for Packet 19: 8.83e-09 V²/Hz
Mean PSD Value for Packet 20: 8.80e-09 V²/Hz
Mean PSD Value for Packet 21: 8.78e-09 V²/Hz
Mean PSD Value for Packet 22: 8.80e-09 V²/Hz
Mean PSD Value for Packet 23: 8.68e-09 V²/Hz
Mean PSD Value for Packet 24: 8.91e-09 V²/Hz
Mean PSD Value for Packet 25: 8.89e-09 V²/Hz
Mean PSD Value for Packet 26: 8.84e-09 V²/Hz
Mean PSD Value for Packet 27: 8.87e-09 V²/Hz
Mean PSD Value for Packet 28: 9.03e-09 V²/Hz
- (Optional) Plots the log-scale PSD spectrum, centered around 0 Hz.
- Helps verify:
  - If frequency correction was successful.
  - Signal’s power concentration and SNR quality.

# Step6: Frequency Spectrum Analysis of Corrected Signal Packets

## 🛠️ Working Procedure
### 🎯 Objective
To analyze the frequency characteristics of each corrected signal packet using FFT and identify the dominant (peak) frequency.
### 📋 Steps Involved
1. FFT Calculation
   Apply FFT to each corrected signal packet to convert the time-domain signal into the frequency domain.
2. Spectrum Centering
   Use fftshift to center the frequency spectrum around 0 Hz for easier interpretation.
3. Frequency Axis Calculation
   Generate the corresponding frequency axis using the sampling rate and FFT size.
4. Peak Frequency Detection
   Identify the frequency bin with the highest magnitude and convert it into kHz.
5. (Optional) Spectrum Visualization
   Plot the magnitude spectrum with ±10 MHz lines to visually inspect the frequency content.

## 🧾 Python Code
import numpy as np
import matplotlib.pyplot as plt

def plot_frequency_spectrum(corrected_packet, idx, Fs, fft_size=2048):
    """Compute and plot the frequency spectrum of a corrected packet using a specified FFT size."""
    spectrum = np.fft.fftshift(np.abs(np.fft.fft(corrected_packet, n=fft_size)))
    freq_axis = np.fft.fftshift(np.fft.fftfreq(fft_size, d=1/Fs))

    # Find peak frequency in kHz
    peak_freq = freq_axis[np.argmax(spectrum)] / 1e3
    '''
    plt.figure(figsize=(10, 4))
    plt.plot(freq_axis / 1e6, spectrum)
    plt.axvline(x=-10, color='red', linestyle='--', linewidth=1, label='-10 MHz')
    plt.axvline(x=10, color='red', linestyle='--', linewidth=1, label='10 MHz')
    plt.title(f"Frequency Spectrum of Corrected Packet {idx} (Peak: {peak_freq:.2f} kHz)")
    plt.xlabel("Frequency [MHz]")
    plt.ylabel("Magnitude")
    plt.legend()
    plt.tight_layout()
    plt.show()
    '''
    print(f"Packet {idx}: Peak Frequency = {peak_freq:.2f} kHz")

def plot_spectra_from_corrected_packets(corrected_packets, sampling_rate):
    """Plots frequency spectra for all already corrected packets."""
    for idx, packet in enumerate(corrected_packets, start=1):
        plot_frequency_spectrum(packet, idx, sampling_rate)

# --- Call the function directly using your stored corrected_packets list ---
plot_spectra_from_corrected_packets(corrected_packets, sampling_rate)

## 📈 Output
For each corrected packet:
- ✅ Prints:
- Packet 1: Peak Frequency = 5175.78 kHz
- Packet 2: Peak Frequency = 6582.03 kHz
- Packet 3: Peak Frequency = 2968.75 kHz
- Packet 4: Peak Frequency = 2968.75 kHz
- Packet 5: Peak Frequency = 2578.12 kHz
- Packet 6: Peak Frequency = 6679.69 kHz
- Packet 7: Peak Frequency = 2519.53 kHz
- Packet 8: Peak Frequency = 2578.12 kHz
- Packet 9: Peak Frequency = 2519.53 kHz
- Packet 10: Peak Frequency = 4824.22 kHz
- Packet 11: Peak Frequency = 3007.81 kHz
- Packet 12: Peak Frequency = 2871.09 kHz
- Packet 13: Peak Frequency = 4023.44 kHz
- Packet 14: Peak Frequency = 2441.41 kHz
- Packet 15: Peak Frequency = 2988.28 kHz
- Packet 16: Peak Frequency = 2851.56 kHz
- Packet 17: Peak Frequency = 2890.62 kHz
- Packet 18: Peak Frequency = 2988.28 kHz
- Packet 19: Peak Frequency = 2988.28 kHz

for ocusync2 data:
- Packet 1: Peak Frequency = 6665.04 kHz
- Packet 2: Peak Frequency = 8740.23 kHz
- Packet 3: Peak Frequency = -683.59 kHz
- Packet 4: Peak Frequency = -1147.46 kHz
- Packet 5: Peak Frequency = 8813.48 kHz
- Packet 6: Peak Frequency = 3271.48 kHz
- Packet 7: Peak Frequency = 5004.88 kHz
- Packet 8: Peak Frequency = 4760.74 kHz
- Packet 9: Peak Frequency = 4687.50 kHz
- Packet 10: Peak Frequency = -415.04 kHz
- Packet 11: Peak Frequency = 5224.61 kHz
- Packet 12: Peak Frequency = 7812.50 kHz
- Packet 13: Peak Frequency = -4077.15 kHz
- Packet 14: Peak Frequency = 7812.50 kHz
- Packet 15: Peak Frequency = 8593.75 kHz
- Packet 16: Peak Frequency = 8374.02 kHz
- Packet 17: Peak Frequency = 4370.12 kHz
- Packet 18: Peak Frequency = -73.24 kHz
- Packet 19: Peak Frequency = 8325.20 kHz
- Packet 20: Peak Frequency = 4882.81 kHz
- Packet 21: Peak Frequency = 7641.60 kHz
- Packet 22: Peak Frequency = 6835.94 kHz
- Packet 23: Peak Frequency = 3955.08 kHz
- Packet 24: Peak Frequency = 4638.67 kHz
- Packet 25: Peak Frequency = 4760.74 kHz
- ...
- Packet 98: Peak Frequency = 7714.84 kHz
- Packet 99: Peak Frequency = 7568.36 kHz
- Packet 100: Peak Frequency = -1464.84 kHz
- Packet 101: Peak Frequency = 6323.24 kHz
for ocusync3 data:
Packet 1: Peak Frequency = -1621.09 kHz
Packet 2: Peak Frequency = -4238.28 kHz
Packet 3: Peak Frequency = -1308.59 kHz
Packet 4: Peak Frequency = -3359.38 kHz
Packet 5: Peak Frequency = -1855.47 kHz
Packet 6: Peak Frequency = -3671.88 kHz
Packet 7: Peak Frequency = -1640.62 kHz
Packet 8: Peak Frequency = 3378.91 kHz
Packet 9: Peak Frequency = -1855.47 kHz
Packet 10: Peak Frequency = -1542.97 kHz
Packet 11: Peak Frequency = -2460.94 kHz
Packet 12: Peak Frequency = -1523.44 kHz
Packet 13: Peak Frequency = -1542.97 kHz
Packet 14: Peak Frequency = -1210.94 kHz
Packet 15: Peak Frequency = -1542.97 kHz
Packet 16: Peak Frequency = -1523.44 kHz
Packet 17: Peak Frequency = -1601.56 kHz
Packet 18: Peak Frequency = -7636.72 kHz
Packet 19: Peak Frequency = -1210.94 kHz
Packet 20: Peak Frequency = -1210.94 kHz
Packet 21: Peak Frequency = -1445.31 kHz
Packet 22: Peak Frequency = -1464.84 kHz
Packet 23: Peak Frequency = -2148.44 kHz
Packet 24: Peak Frequency = -1210.94 kHz
Packet 25: Peak Frequency = -1835.94 kHz
Packet 26: Peak Frequency = -3632.81 kHz
Packet 27: Peak Frequency = -1523.44 kHz
Packet 28: Peak Frequency = -3359.38 kHz
- 📊 (Optional) Displays:
  - Frequency spectrum plot (if plotting section is uncommented).
  - Vertical lines at ±10 MHz for visual reference.

## 💡 Purpose & Use Case
This routine is useful for:
- ✅ Verifying frequency offset correction effectiveness.
- ✅ Identifying dominant frequency components in packets.

# Step7:DFT-Based Filtering of Frequency-Corrected Packets

## 🛠️ Working Procedure
### 🎯 Objective
To apply a low-pass filter in the frequency domain (DFT-based) to remove noise on already frequency-corrected signal packets and optionally visualize their spectrograms.
### 📋 Steps Involved
1. Band Selection by User
  1. The user selects a band (Option 1, 2, or 3).
  2. Based on selection, a cutoff frequency is set.
2. DFT-Based Filtering
  1. The FFT (DFT) of the signal is computed.
  2. A mask is applied in the frequency domain to keep only frequencies below the selected cutoff.
  3. The inverse FFT is used to transform the filtered signal back to the time domain.
3. Packet Storage
  1. Each filtered packet is stored in a list for further analysis or visualization.
4. (Optional) Spectrogram Visualization
  1. Spectrograms can be plotted to inspect the time-frequency content of the filtered packets.

## 🧾 Python Code
import numpy as np
import matplotlib.pyplot as plt
import scipy.signal
from scipy.signal import butter, filtfilt, welch, hamming

# Function for DFT-based filtering
def dft_filter(signal: np.ndarray, cutoff: float, sampling_rate: float):
    """
    Apply a DFT-based low-pass filter to the signal.
    """
    dft = np.fft.fft(signal)
    freqs = np.fft.fftfreq(len(signal), d=1/sampling_rate)
    filter_mask = np.abs(freqs) < cutoff
    dft_filtered = dft * filter_mask
    signal_filtered = np.fft.ifft(dft_filtered)
    return signal_filtered

# Prompt user for selection
selection = input("Press 1, 2, or 3 to select the band: ").strip()
if selection not in ["1", "2", "3"]:
    print("Invalid selection. Defaulting to 1.")
    selection = "1"

# Define cutoff frequency and sampling rate based on selection
sampling_rate_mapping = {"1": 40e6, "2": 50e6, "3": 40e6}
cutoff_mapping = {"1": 7.5e6, "2": 8.5e6, "3": 8.5e6}

sampling_rate = sampling_rate_mapping[selection]
cutoff_freq = cutoff_mapping[selection]

# Initialize dictionary to store filtered packets with metadata
filtered_packet_storage = {}

# Initialize list to store only the selected filtered packets
filtered_packets = []

# Use already corrected packets
for idx, corrected_packet in enumerate(corrected_packets, start=1):
    # Apply DFT-based filter
    filtered_packet = dft_filter(corrected_packet, cutoff_freq, sampling_rate)

    # Store the filtered packet
    filtered_packets.append(filtered_packet)

# Save the filtered packets and cutoff frequency in dictionary
filtered_packet_storage[selection] = {
    "packets": filtered_packets,
    "cutoff_freq": cutoff_freq,
    "sampling_rate": sampling_rate
}

# Optional: print confirmation
print(f"Stored {len(filtered_packets)} filtered packets for selection {selection} with cutoff {cutoff_freq/1e6} MHz")

## 📈Outcome
- ✅ Filtered Packets: Only frequency components below the selected cutoff (7.5 or 8.5 MHz) remain in the filtered signal.
- 🧠 Spectrogram (Optional):
  - Visual confirmation of the band-pass effect.
  - Noise or unwanted bands outside the cutoff are attenuated.

## 📌 Use Case
- Useful for preprocessing before pattern detection.
- Helps in removing high-frequency noise.
- Supports analysis of band-specific signal behavior.

## Step8: Frequency Spectrum Visualization of Filtered Signal Packets
### 🎯 Objective
To analyze the frequency content of filtered signal packets by computing and visualizing their magnitude spectrum using FFT and fftshift.

## ⚙️ Working Procedure
### 🔹 Step 1: Compute FFT
Take the Fast Fourier Transform (FFT) of the signal to convert it from the time domain to the frequency domain.
### 🔹 Step 2: Apply fftshift
Rearrange the FFT output so that 0 Hz is centered on the frequency axis, showing negative and positive frequencies symmetrically.
### 🔹 Step 3: Build Frequency Axis
Use np.fft.fftfreq() to generate the frequency bins and apply fftshift for alignment with the spectrum.
### 🔹 Step 4: (Optional) Plot
- The plot section is currently commented out but allows visualization of the magnitude spectrum.
- Vertical lines at ±10 MHz serve as reference bounds.

## 💻 Python Code
import numpy as np
import matplotlib.pyplot as plt
from scipy.signal import welch, hamming

# Function to plot frequency spectrum using fftshift
def plot_frequency_spectrum(signal, sampling_rate, idx, fft_size=2048):
    """Computes and plots the frequency spectrum of the given signal using FFT shift."""
    spectrum = np.fft.fftshift(np.abs(np.fft.fft(signal, n=fft_size)))
    freq_axis = np.fft.fftshift(np.fft.fftfreq(fft_size, d=1/sampling_rate))
    '''
    plt.figure(figsize=(10, 4))
    plt.plot(freq_axis / 1e6, spectrum) # Convert frequency to MHz
    plt.axvline(x=-10, color='red', linestyle='--', linewidth=1, label='-10 MHz')
    plt.axvline(x=10, color='red', linestyle='--', linewidth=1, label='10 MHz')
    plt.title(f"Frequency Spectrum of Filtered Packet {idx}")
    plt.xlabel("Frequency [MHz]")
    plt.ylabel("Magnitude")
    plt.legend()
    plt.show()
    '''

# Plot spectrum of already filtered packets
for idx, filtered_packet in enumerate(filtered_packets, start=1):
    plot_frequency_spectrum(filtered_packet, sampling_rate, idx)

## ✅ Outcome
- You get the magnitude spectrum of each filtered packet.
- Optional plots (when uncommented) give a clear view of frequency spread, helping verify whether unwanted frequency components were successfully removed by filtering.

## 📈 Power Spectral Density (PSD) Analysis of Filtered Signal Packets
### 🎯 Objective
To analyze the spectral power distribution of signal packets after applying DFT-based filtering, which helps in verifying the filtering effect and characterizing the remaining signal content.

## ⚙️ Working Procedure
### 🔹 Step 1: Loop Over Packets
Iterate through all filtered signal packets for PSD computation.
### 🔹 Step 2: Apply Hamming Window
Use a Hamming window to reduce spectral leakage before performing the spectral estimate.
### 🔹 Step 3: Compute PSD (Welch's Method)
Estimate the PSD using scipy.signal.welch() with specified FFT points (nfft_welch) and frequency bins.
### 🔹 Step 4: Center the Frequency Axis
Use fftshift to center the PSD around 0 Hz for visual clarity.
### 🔹 Step 5: Output Mean PSD
Print the mean value of the PSD for quick inspection or thresholding.
### 🔹 (Optional) Step 6: Plot
Commented section allows plotting the PSD on a logarithmic y-scale for better visibility of weaker components.

## 💻 Python Code
import numpy as np
import matplotlib.pyplot as plt
from scipy.signal import welch, hamming

# Parameters
nfft_welch = 1024 # Number of FFT points for Welch's method

def compute_and_plot_psd_from_filtered(filtered_packets, sampling_rate):
    """
    Computes and plots the Power Spectral Density (PSD) of already filtered packets.

    Parameters:
        filtered_packets (list): List of already filtered packets (complex baseband).
        sampling_rate (float): Sampling frequency in Hz.
    """
    for idx, packet in enumerate(filtered_packets, start=1):
        if len(packet) < nfft_welch:
        print(f"Packet {idx}: Insufficient data length for Welch's method")
        continue

        # Apply Hamming window
        window = hamming(len(packet))
        data_windowed = packet * window

        # Compute PSD using Welch's method
        f, Pxx_den = welch(data_windowed, sampling_rate, nperseg=nfft_welch, return_onesided=False)

        # Shift frequency and PSD for negative frequencies
        Pxx_den_shifted = np.fft.fftshift(Pxx_den)
        f_shifted = np.fft.fftshift(f)

        # Compute mean PSD value
        mean_psd_value = np.mean(Pxx_den_shifted)
        print(f"Mean PSD Value for Packet {idx}: {mean_psd_value:.2e} V^2/Hz")
        '''
        # Plot PSD
        plt.figure(figsize=(8, 3))
        plt.semilogy(f_shifted / 1e6, Pxx_den_shifted) # Convert frequency to MHz
        plt.axhline(1.1 * mean_psd_value, color='r', linestyle='--', label="Mean PSD")
        plt.xlabel("Frequency [MHz]")
        plt.ylabel("PSD [V**2/Hz]")
        plt.title(f"Power Spectral Density (PSD) of Filtered Packet {idx}")
        plt.legend()
        plt.tight_layout()
        plt.show()
        '''

# Call function with your data
compute_and_plot_psd_from_filtered(filtered_packets, sampling_rate)

## ✅Outcome
For each filtered signal packet, the mean PSD value will be printed.
Mean PSD Value for Packet 1: 5.06e-09 V^2/Hz
Mean PSD Value for Packet 2: 4.99e-09 V^2/Hz
Mean PSD Value for Packet 3: 3.86e-09 V^2/Hz
Mean PSD Value for Packet 4: 5.05e-09 V^2/Hz
Mean PSD Value for Packet 5: 3.59e-09 V^2/Hz
Mean PSD Value for Packet 6: 3.98e-09 V^2/Hz
Mean PSD Value for Packet 7: 4.07e-09 V^2/Hz
Mean PSD Value for Packet 8: 3.45e-09 V^2/Hz
Mean PSD Value for Packet 9: 4.88e-09 V^2/Hz
Mean PSD Value for Packet 10: 4.42e-09 V^2/Hz
Mean PSD Value for Packet 11: 4.08e-09 V^2/Hz
Mean PSD Value for Packet 12: 4.65e-09 V^2/Hz
Mean PSD Value for Packet 13: 4.19e-09 V^2/Hz
Mean PSD Value for Packet 14: 4.13e-09 V^2/Hz
Mean PSD Value for Packet 15: 4.16e-09 V^2/Hz
Mean PSD Value for Packet 16: 4.07e-09 V^2/Hz
Mean PSD Value for Packet 17: 4.53e-09 V^2/Hz
Mean PSD Value for Packet 18: 3.98e-09 V^2/Hz
Mean PSD Value for Packet 19: 4.12e-09 V^2/Hz

for ocusync2 data:
Mean PSD Value for Packet 1: 1.71e-12 V^2/Hz
Mean PSD Value for Packet 2: 1.73e-12 V^2/Hz
Mean PSD Value for Packet 3: 1.71e-12 V^2/Hz
Mean PSD Value for Packet 4: 1.73e-12 V^2/Hz
Mean PSD Value for Packet 5: 1.74e-12 V^2/Hz
Mean PSD Value for Packet 6: 1.76e-12 V^2/Hz
Mean PSD Value for Packet 7: 1.73e-12 V^2/Hz
Mean PSD Value for Packet 8: 1.70e-12 V^2/Hz
Mean PSD Value for Packet 9: 1.67e-12 V^2/Hz
Mean PSD Value for Packet 10: 1.67e-12 V^2/Hz
Mean PSD Value for Packet 11: 1.67e-12 V^2/Hz
Mean PSD Value for Packet 12: 1.66e-12 V^2/Hz
Mean PSD Value for Packet 13: 1.65e-12 V^2/Hz
Mean PSD Value for Packet 14: 1.67e-12 V^2/Hz
Mean PSD Value for Packet 15: 1.71e-12 V^2/Hz
Mean PSD Value for Packet 16: 1.77e-12 V^2/Hz
Mean PSD Value for Packet 17: 1.78e-12 V^2/Hz
Mean PSD Value for Packet 18: 1.81e-12 V^2/Hz
Mean PSD Value for Packet 19: 1.82e-12 V^2/Hz
Mean PSD Value for Packet 20: 1.81e-12 V^2/Hz
Mean PSD Value for Packet 21: 1.78e-12 V^2/Hz
Mean PSD Value for Packet 22: 1.77e-12 V^2/Hz
Mean PSD Value for Packet 23: 1.73e-12 V^2/Hz
Mean PSD Value for Packet 24: 1.71e-12 V^2/Hz
Mean PSD Value for Packet 25: 1.70e-12 V^2/Hz
...
Mean PSD Value for Packet 98: 1.75e-12 V^2/Hz
Mean PSD Value for Packet 99: 1.76e-12 V^2/Hz
Mean PSD Value for Packet 100: 1.77e-12 V^2/Hz
Mean PSD Value for Packet 101: 1.79e-12 V^2/Hz

for ocusync3 data:
Mean PSD Value for Packet 1: 9.95e-09 V^2/Hz
Mean PSD Value for Packet 2: 9.84e-09 V^2/Hz
Mean PSD Value for Packet 3: 9.67e-09 V^2/Hz
Mean PSD Value for Packet 4: 9.71e-09 V^2/Hz
Mean PSD Value for Packet 5: 9.17e-09 V^2/Hz
Mean PSD Value for Packet 6: 9.09e-09 V^2/Hz
Mean PSD Value for Packet 7: 9.11e-09 V^2/Hz
Mean PSD Value for Packet 8: 8.97e-09 V^2/Hz
Mean PSD Value for Packet 9: 8.82e-09 V^2/Hz
Mean PSD Value for Packet 10: 8.82e-09 V^2/Hz
Mean PSD Value for Packet 11: 8.39e-09 V^2/Hz
Mean PSD Value for Packet 12: 8.45e-09 V^2/Hz
Mean PSD Value for Packet 13: 8.47e-09 V^2/Hz
Mean PSD Value for Packet 14: 8.31e-09 V^2/Hz
Mean PSD Value for Packet 15: 8.13e-09 V^2/Hz
Mean PSD Value for Packet 16: 8.16e-09 V^2/Hz
Mean PSD Value for Packet 17: 7.77e-09 V^2/Hz
Mean PSD Value for Packet 18: 7.90e-09 V^2/Hz
Mean PSD Value for Packet 19: 7.95e-09 V^2/Hz
Mean PSD Value for Packet 20: 7.87e-09 V^2/Hz
Mean PSD Value for Packet 21: 7.85e-09 V^2/Hz
Mean PSD Value for Packet 22: 7.90e-09 V^2/Hz
Mean PSD Value for Packet 23: 7.76e-09 V^2/Hz
Mean PSD Value for Packet 24: 7.95e-09 V^2/Hz
Mean PSD Value for Packet 25: 7.95e-09 V^2/Hz
Mean PSD Value for Packet 26: 7.90e-09 V^2/Hz
Mean PSD Value for Packet 27: 7.95e-09 V^2/Hz
Mean PSD Value for Packet 28: 8.14e-09 V^2/Hz
- Optional PSD plots show the signal’s power distribution across frequency.
- These plots are useful for:
  - Identifying dominant frequency components.
  - Verifying the effect of filtering.
  - Detecting residual noise or unwanted harmonics.
  - clean PSD helps estimate signal power accurately.

## Step9: SNR Analysis of Filtered Signal Packets

### ⚙️ Working Procedure
This procedure is used to analyze signal packets that have already been filtered (e.g., using a bandpass filter or DFT-based filter). It focuses on measuring the SNR and visualizing the PSD of the filtered packets.
#### 🔄 Steps:
1. Filtered Packet Selection:
  1. User selects from previously filtered signal packets stored in a dictionary under keys "1", "2", and "3".
  2. Each entry includes:
    1. packets: list of filtered signal packets
    2. cutoff_freq: applied cutoff frequency during filtering
    3. sampling_rate: sample rate of acquisition
2. PSD Computation:
  1. Apply a Hamming window to reduce spectral leakage.
  2. Use Welch’s method with FFT (nfft=2048) to compute the PSD.
3. Frequency Band Definition:
  1. Signal Band: from -cutoff_freq to +cutoff_freq
  2. Noise Band:
    1. Lower Band: from -sampling_rate/2 to -cutoff_freq
    2. Upper Band: from +cutoff_freq to +sampling_rate/2
4. SNR Computation:
  1. Integrate the power in the signal and noise bands using np.trapz.
  2. Compute SNR in dB using the formula:
    SNR(dB)=10⋅log⁡10(Signal Power / Noise Power)
5. (Optional) Plot PSD:
  1. Display power vs frequency.
  2. Highlight signal and noise bands for clarity.

## 💻 Python Code
import numpy as np
import matplotlib.pyplot as plt
from scipy.signal import welch, hamming

def integrate_power(frequencies, psd, band):
    """Integrate power over a specified frequency band."""
    indices = (frequencies >= band[0]) & (frequencies <= band[1])
    return np.trapz(psd[indices], frequencies[indices])

def compute_snr_and_plot_psd_filtered(filtered_packet_storage, selection):
    """
    Computes the SNR and plots the PSD for pre-filtered packets from storage.

    Parameters:
    - filtered_packet_storage: Dictionary with keys "1", "2", or "3", each containing:
        - "packets": list of filtered signal packets
        - "cutoff_freq": filter cutoff frequency used
        - "sampling_rate": sampling rate in Hz
    - selection: User input to select which packet set to analyze
    """
    if selection not in filtered_packet_storage:
        print(f"No filtered packets found for selection {selection}.")
        return

    stored = filtered_packet_storage[selection]
    filtered_packets = stored["packets"]
    cutoff_frequency = stored["cutoff_freq"]
    sampling_rate = stored["sampling_rate"]

    nfft_welch = 2048

    # Define frequency bands
    signal_band = (-cutoff_frequency, cutoff_frequency)
    noise_band_lower = (-sampling_rate / 2, -cutoff_frequency)
    noise_band_upper = (cutoff_frequency, sampling_rate / 2)

    for idx, filtered_packet in enumerate(filtered_packets, start=1):
        if len(filtered_packet) < nfft_welch:
        print(f"Packet {idx}: Insufficient data length for Welch's method.")
        continue

        # Apply Hamming window
        window = hamming(len(filtered_packet))
        data_windowed = filtered_packet * window

        # Welch PSD
        f, Pxx_den = welch(data_windowed, sampling_rate, nperseg=nfft_welch, return_onesided=False)
        Pxx_den_shifted = np.fft.fftshift(Pxx_den)
        f_shifted = np.fft.fftshift(f)

        # Power calculation
        signal_power = integrate_power(f_shifted, Pxx_den_shifted, signal_band)
        noise_power_lower = integrate_power(f_shifted, Pxx_den_shifted, noise_band_lower)
        noise_power_upper = integrate_power(f_shifted, Pxx_den_shifted, noise_band_upper)
        total_noise_power = noise_power_lower + noise_power_upper

        # SNR calculation
        if total_noise_power > 0:
        snr_dB = 10 * np.log10(signal_power / total_noise_power)
        print(f"Packet {idx}: SNR = {snr_dB:.2f} dB")
        else:
        print(f"Packet {idx}: Noise power too low, SNR cannot be computed.")

        '''
        # Optional PSD plot
        plt.figure(figsize=(8, 4))
        plt.semilogy(f_shifted / 1e6, Pxx_den_shifted, label="PSD")
        plt.axhline(1.1 * np.mean(Pxx_den_shifted), color='r', linestyle='--', label="Mean PSD")
        plt.axvspan(signal_band[0]/1e6, signal_band[1]/1e6, color='green', alpha=0.3, label="Signal Band")
        plt.axvspan(noise_band_lower[0]/1e6, noise_band_lower[1]/1e6, color='red', alpha=0.3, label="Noise Lower")
        plt.axvspan(noise_band_upper[0]/1e6, noise_band_upper[1]/1e6, color='blue', alpha=0.3, label="Noise Upper")
        plt.xlabel("Frequency [MHz]")
        plt.ylabel("PSD [V^2/Hz]")
        plt.title(f"PSD of Filtered Packet {idx} (Selection {selection})")
        plt.legend()
        plt.grid(True)
        plt.tight_layout()
        plt.show()
        '''

# Example interaction
selection = input("Press 1, 2, or 3 to select the filtered packet: ").strip()
if selection not in ["1", "2", "3"]:
    print("Invalid selection. Defaulting to 1.")
    selection = "1"

compute_snr_and_plot_psd_filtered(filtered_packet_storage, selection)

### ✅ Outcome
SNR is printed for each packet in decibels (dB), giving a measure of how much cleaner the signal became after filtering.
SNR for filtered signal packets
For ocusync1 data:
Packet 1: SNR = 31.50 dB
Packet 2: SNR = 32.81 dB
Packet 3: SNR = 32.79 dB
Packet 4: SNR = 31.87 dB
Packet 5: SNR = 31.92 dB
Packet 6: SNR = 32.60 dB
Packet 7: SNR = 32.51 dB
Packet 8: SNR = 32.76 dB
Packet 9: SNR = 32.08 dB
Packet 10: SNR = 33.26 dB
Packet 11: SNR = 32.68 dB
Packet 12: SNR = 32.28 dB
Packet 13: SNR = 32.38 dB
Packet 14: SNR = 32.84 dB
Packet 15: SNR = 32.70 dB
Packet 16: SNR = 31.96 dB
Packet 17: SNR = 32.48 dB
Packet 18: SNR = 32.24 dB
Packet 19: SNR = 32.29 dB

for ocusync2 data:
Packet 1: SNR = 38.89 dB
Packet 2: SNR = 39.60 dB
Packet 3: SNR = 38.75 dB
Packet 4: SNR = 38.81 dB
Packet 5: SNR = 39.70 dB
Packet 6: SNR = 39.13 dB
Packet 7: SNR = 39.47 dB
Packet 8: SNR = 39.64 dB
Packet 9: SNR = 38.82 dB
Packet 10: SNR = 39.06 dB
Packet 11: SNR = 39.47 dB
Packet 12: SNR = 39.91 dB
Packet 13: SNR = 39.58 dB
Packet 14: SNR = 39.61 dB
Packet 15: SNR = 39.16 dB
Packet 16: SNR = 39.26 dB
Packet 17: SNR = 39.91 dB
Packet 18: SNR = 40.78 dB
Packet 19: SNR = 39.98 dB
Packet 20: SNR = 39.35 dB
Packet 21: SNR = 39.59 dB
Packet 22: SNR = 39.36 dB
Packet 23: SNR = 40.07 dB
Packet 24: SNR = 38.66 dB
Packet 25: SNR = 39.41 dB
...
Packet 98: SNR = 39.33 dB
Packet 99: SNR = 39.37 dB
Packet 100: SNR = 38.87 dB
Packet 101: SNR = 39.19 dB
for ocusync3 data:
Packet 1: SNR = 41.96 dB
Packet 2: SNR = 42.13 dB
Packet 3: SNR = 41.22 dB
Packet 4: SNR = 40.65 dB
Packet 5: SNR = 42.12 dB
Packet 6: SNR = 38.97 dB
Packet 7: SNR = 40.73 dB
Packet 8: SNR = 39.68 dB
Packet 9: SNR = 40.15 dB
Packet 10: SNR = 40.22 dB
Packet 11: SNR = 41.45 dB
Packet 12: SNR = 40.15 dB
Packet 13: SNR = 42.62 dB
Packet 14: SNR = 43.38 dB
Packet 15: SNR = 38.59 dB
Packet 16: SNR = 41.32 dB
Packet 17: SNR = 42.46 dB
Packet 18: SNR = 40.82 dB
Packet 19: SNR = 42.24 dB
Packet 20: SNR = 41.74 dB
Packet 21: SNR = 43.62 dB
Packet 22: SNR = 38.78 dB
Packet 23: SNR = 41.79 dB
Packet 24: SNR = 42.24 dB
Packet 25: SNR = 40.69 dB
Packet 26: SNR = 41.23 dB
Packet 27: SNR = 41.68 dB
Packet 28: SNR = 39.53 dB
- (Optional) PSD plots can be generated for each filtered packet showing:
  - Signal band (highlighted in green)
  - Noise bands (highlighted in red and blue)
  - Power concentration across the frequency spectrum
This confirms that filtering has successfully isolated the desired band and suppressed noise outside it.

## Step10:Moment-Based Skewness and Kurtosis Analysis of Filtered Signal Packets

### ⚙️ Working Procedure
This script analyzes filtered signal packets by calculating skewness and kurtosis using moment-based statistical measures. It is particularly useful to classify the distribution type of each filtered packet and understand the asymmetry and tail behavior in signal amplitudes.
#### 🔬 Definitions:
- After filtering the corrected signal packets, we calculated the skewness and kurtosis using the following formulas:
  Skewness: Skewness = (n / ((n-1)(n-2))) * Σ ((x_i - μ) / σ)³
  Kurtosis: Kurtosis = (1 / n) * Σ ((x_i - μ) / σ)⁴ - 3
  Where:
- nn is the number of samples in the signal,
- xi is each individual data point,
- μ is the mean of the signal,
- σ is the standard deviation.
#### 📦 Steps:
1. User Selection:
  1. The user selects one of the filtered packet sets ("1", "2", "3").
2. (Optional) KDE Plot:
  1. A Kernel Density Estimate (KDE) plot visualizes the probability distribution of the packet's amplitude.

## 💻 Python Code
import numpy as np
import seaborn as sns
import matplotlib.pyplot as plt

def moment_based_skew(signal_packet):
    """Compute moment-based skewness of the signal packet (magnitude used if complex)."""
    signal_packet = np.abs(signal_packet)
    n = len(signal_packet)
    mean = np.mean(signal_packet)
    std = np.std(signal_packet)
    skewness = (n / ((n - 1) * (n - 2))) * np.sum(((signal_packet - mean) / std) ** 3)
    return skewness

def moment_based_kurtosis(signal_packet):
    """Compute moment-based excess kurtosis of the signal packet (magnitude used if complex)."""
    signal_packet = np.abs(signal_packet)
    n = len(signal_packet)
    mean = np.mean(signal_packet)
    std = np.std(signal_packet)
    kurtosis = (1 / n) * np.sum(((signal_packet - mean) / std) ** 4) - 3
    return kurtosis

def process_packet(filtered_packet, idx):
    """Compute skewness, kurtosis, and plot KDE for the given filtered packet."""
    skewness = moment_based_skew(filtered_packet)
    kurtosis_value = moment_based_kurtosis(filtered_packet)

    print(f"Packet {idx}: Skewness = {skewness:.4f}, Kurtosis = {kurtosis_value:.4f}")

    '''
    # KDE Plot for packet
    plt.figure(figsize=(8, 3))
    sns.kdeplot(np.abs(filtered_packet), label=f"Packet {idx} KDE", fill=True)
    plt.title(f"Packet {idx} KDE\nSkew: {skewness:.4f} | Kurtosis: {kurtosis_value:.4f}")
    plt.xlabel("Amplitude")
    plt.ylabel("Density")
    plt.legend(loc='upper right')
    plt.grid(True)
    plt.tight_layout()
    plt.show()
    '''

# Prompt user for selection
selection = input("Press 1, 2, or 3 to select the stored filtered packet set: ").strip()
if selection not in ["1", "2", "3"]:
    print("Invalid selection. Defaulting to 1.")
    selection = "1"

# Access packets from the structured dictionary
packet_entry = filtered_packet_storage.get(selection)

if packet_entry is None or "packets" not in packet_entry:
    print(f"No stored packets found for selection {selection}.")
else:
    selected_filtered_packets = packet_entry["packets"]
    for idx, filtered_packet in enumerate(selected_filtered_packets, start=1):
        process_packet(filtered_packet, idx)

### ✅ Outcome
For each filtered signal packet:
📈 Skewness and Kurtosis values are printed.
Packet 1: Skewness = 0.1044, Kurtosis = -0.7564
Packet 2: Skewness = 0.1089, Kurtosis = -0.7378
Packet 3: Skewness = 0.2634, Kurtosis = -0.5786
Packet 4: Skewness = 0.1287, Kurtosis = -0.7455
Packet 5: Skewness = 0.3208, Kurtosis = -0.4856
Packet 6: Skewness = 0.2170, Kurtosis = -0.6613
Packet 7: Skewness = 0.1827, Kurtosis = -0.7175
Packet 8: Skewness = 0.3244, Kurtosis = -0.4703
Packet 9: Skewness = 0.1315, Kurtosis = -0.7666
Packet 10: Skewness = 0.1225, Kurtosis = -0.7651
Packet 11: Skewness = 0.1409, Kurtosis = -0.7394
Packet 12: Skewness = 0.0748, Kurtosis = -0.8155
Packet 13: Skewness = 0.1380, Kurtosis = -0.7674
Packet 14: Skewness = 0.1282, Kurtosis = -0.7661
Packet 15: Skewness = 0.1028, Kurtosis = -0.8030
Packet 16: Skewness = 0.1551, Kurtosis = -0.7365
Packet 17: Skewness = 0.1344, Kurtosis = -0.7672
Packet 18: Skewness = 0.1970, Kurtosis = -0.7002
Packet 19: Skewness = 0.1292, Kurtosis = -0.7543

for ocusync2 data:
Packet 1: Skewness = 0.5990, Kurtosis = 0.5545
Packet 2: Skewness = 0.6225, Kurtosis = 0.6272
 Packet 3: Skewness = 0.5885, Kurtosis = 0.5041
Packet 4: Skewness = 0.5927, Kurtosis = 0.5521
Packet 5: Skewness = 0.6014, Kurtosis = 0.5592
Packet 6: Skewness = 0.6122, Kurtosis = 0.5967
Packet 7: Skewness = 0.6059, Kurtosis = 0.5397
Packet 8: Skewness = 0.6157, Kurtosis = 0.6335
Packet 9: Skewness = 0.6127, Kurtosis = 0.5908
Packet 10: Skewness = 0.6161, Kurtosis = 0.6052
Packet 11: Skewness = 0.6060, Kurtosis = 0.5348
Packet 12: Skewness = 0.6053, Kurtosis = 0.5710
Packet 13: Skewness = 0.6094, Kurtosis = 0.5761
Packet 14: Skewness = 0.5835, Kurtosis = 0.5050
Packet 15: Skewness = 0.6097, Kurtosis = 0.5493
Packet 16: Skewness = 0.6158, Kurtosis = 0.6372
Packet 17: Skewness = 0.6210, Kurtosis = 0.6095
Packet 18: Skewness = 0.6139, Kurtosis = 0.5967
Packet 19: Skewness = 0.6083, Kurtosis = 0.5780
Packet 20: Skewness = 0.6078, Kurtosis = 0.5883
Packet 21: Skewness = 0.5757, Kurtosis = 0.4774
Packet 22: Skewness = 0.5958, Kurtosis = 0.5393
Packet 23: Skewness = 0.6150, Kurtosis = 0.5606
Packet 24: Skewness = 0.5883, Kurtosis = 0.5226
Packet 25: Skewness = 0.5955, Kurtosis = 0.5225
...
Packet 98: Skewness = 0.5820, Kurtosis = 0.5004
Packet 99: Skewness = 0.5986, Kurtosis = 0.5334
Packet 100: Skewness = 0.5875, Kurtosis = 0.5344
Packet 101: Skewness = 0.5734, Kurtosis = 0.5709

for ocusync3 data:
Packet 1: Skewness = -0.5195, Kurtosis = -0.3159
Packet 2: Skewness = -0.4291, Kurtosis = -0.3603
Packet 3: Skewness = -0.5308, Kurtosis = -0.2652
Packet 4: Skewness = -0.6028, Kurtosis = -0.2017
Packet 5: Skewness = -0.4446, Kurtosis = -0.3687
Packet 6: Skewness = -0.5481, Kurtosis = -0.2710
Packet 7: Skewness = -0.5769, Kurtosis = -0.2022
Packet 8: Skewness = -0.4987, Kurtosis = -0.2772
Packet 9: Skewness = -0.5347, Kurtosis = -0.3054
Packet 10: Skewness = -0.5954, Kurtosis = -0.2554
Packet 11: Skewness = -0.4942, Kurtosis = -0.3053
Packet 12: Skewness = -0.5642, Kurtosis = -0.2121
Packet 13: Skewness = -0.6150, Kurtosis = -0.1158
Packet 14: Skewness = -0.5942, Kurtosis = -0.1280
Packet 15: Skewness = -0.5959, Kurtosis = -0.1417
Packet 16: Skewness = -0.6598, Kurtosis = -0.0997
Packet 17: Skewness = -0.5086, Kurtosis = -0.2842
Packet 18: Skewness = -0.5921, Kurtosis = -0.1122
Packet 19: Skewness = -0.6220, Kurtosis = -0.0904
Packet 20: Skewness = -0.5959, Kurtosis = -0.1210
Packet 21: Skewness = -0.5906, Kurtosis = -0.1341
Packet 22: Skewness = -0.6496, Kurtosis = -0.1124
Packet 23: Skewness = -0.5472, Kurtosis = -0.2108
Packet 24: Skewness = -0.5582, Kurtosis = -0.2097
Packet 25: Skewness = -0.5704, Kurtosis = -0.2344
Packet 26: Skewness = -0.5378, Kurtosis = -0.1986
Packet 27: Skewness = -0.5774, Kurtosis = -0.1746
Packet 28: Skewness = -0.6396, Kurtosis = -0.1394
- 🧠 These values help understand the distribution characteristics of filtered packets:
  - E.g., a packet with high kurtosis and positive skewness might indicate sudden bursts or asymmetric energy patterns.
- 📊 (Optional) A KDE plot can be enabled to visualize the shape of the distribution.

# Step11:Pattern Detection in Filtered Signal Packets Using Matched Filtering and Adaptive Thresholding
## Overview
This document describes the step-by-step methodology to detect and extract signal patterns from filtered signal packets using matched filtering, adaptive thresholding, and peak detection techniques. The process includes correlation-based pattern detection, local statistical analysis for adaptive threshold generation, and spectrogram-based visualization of the extracted signal patterns.

## 1. Initialization and Parameter Definition
### Sampling Rate
Given:
fs=50 MHz
### Pattern Duration
Known pattern duration:
T=70 μs=70×10−6 seconds
### Pattern Length in Samples
N=T*fs

## 2. Reference Pattern Extraction
A known reference pattern is extracted from the first filtered signal packet for use in matched filtering:
r[n]=reference_pattern=x0[n]
where x0[n] is the filtered packet

## 3. Matched Filtering (Cross-Correlation)
Matched filtering is performed between the magnitude of the filtered packet x[n] and the reference pattern r[n]r[n] using cross-correlation:

This operation produces a correlation output c[n]c[n] that identifies the similarity between the filtered signal and the reference pattern.

## 4. Normalization of Correlation Output
The correlation result is normalized:

## 5. Smoothing the Correlation Output
To reduce noise and create a smoother envelope of the correlation, the signal is convolved with a smoothing window:

Here, W is the smoothing window size (e.g., 1000 samples).

## 6. Adaptive Thresholding
To dynamically adapt to local variations in signal power, a local mean and standard deviation are calculated over a sliding window.
### Local Mean
### Local Standard Deviation

### Adaptive Threshold

Where:
- MM is the window size for local statistics (e.g., 9000)
- kk is a scaling constant (e.g., 1.8)

## 7. Peak Detection
Signal peaks are detected from the smoothed correlation where:
        s[n] > T[n]

A minimum width and separation (gap) are enforced between peaks to ensure valid pattern extraction.
8. Pattern Extraction
Each peak corresponds to the starting index of a detected pattern. For each detected index ni, the pattern is extracted:

Where pi[n] is the ith extracted pattern of length N samples.
All extracted patterns are stored in a list for further analysis.
9. Spectrogram Visualization
Each detected pattern is visualized.
The spectrogram helps verify that the extracted segments are distinct, structured signal patterns.
10. Output Summary
The total number of patterns detected across all packets is reported:

## 💻 Python Code
import numpy as np
import matplotlib.pyplot as plt
import scipy.signal as signal

# Prompt user for selection
selection = input("Press 1, 2, or 3 to select the band: ").strip()
if selection not in ["1", "2", "3"]:
    print("Invalid selection. Defaulting to 1.")
    selection = "1"

# Define known parameters
sampling_rate_mapping = {"1": 40e6, "2": 50e6, "3": 40e6}
sampling_rate = sampling_rate_mapping[selection]
pattern_duration = 70e-6 # 70 microseconds
pattern_length = int(pattern_duration * sampling_rate) # 2800 samples (for 40 MHz)

# Set the reference start index based on selection
ref_start_idx_mapping = {"1": 20320, "2": 42084, "3": 15200}
ref_start_idx = ref_start_idx_mapping[selection]

# Extract filtered packet list for selected band
reference_packet = filtered_packet_storage[selection]["packets"]

# Get reference pattern from the first filtered packet
reference_pattern = reference_packet[0][ref_start_idx:ref_start_idx + pattern_length]

# Store all extracted patterns
all_extracted_patterns = []

for packet_idx, filtered_packet in enumerate(reference_packet):
    # Matched filter using cross-correlation
    correlation_result = np.correlate(np.abs(filtered_packet), np.abs(reference_pattern), mode="valid")

    # Normalize correlation result
    correlation_result = correlation_result / np.max(correlation_result)

    # Set parameters based on selection
    if selection == "1":
        window_size = 1300
        adaptive_window = 7000
        k_factor = 1.5
        prominence_factor = 0.7
    elif selection == "3":
        window_size = 300
        adaptive_window = 7000
        k_factor = 1.6
        prominence_factor = 0.9
    else:
        window_size = 1800
        adaptive_window = 10000
        k_factor = 1.7
        prominence_factor = 0.7

    # Smooth the correlation result
    smoothed_correlation = signal.convolve(correlation_result, np.ones(window_size) / window_size, mode='same')

    # Compute adaptive threshold
    local_mean = signal.convolve(smoothed_correlation, np.ones(adaptive_window) / adaptive_window, mode='same')
    local_std = np.sqrt(signal.convolve((smoothed_correlation - local_mean) ** 2, np.ones(adaptive_window) / adaptive_window, mode='same'))
    adaptive_threshold = local_mean + k_factor * local_std

    # Detect peaks
    raw_peaks, _ = signal.find_peaks(
        smoothed_correlation,
        height=adaptive_threshold,
        prominence=np.std(smoothed_correlation) * prominence_factor,
        width=100
    )

    # Filter peaks to maintain minimum gap
    min_gap = pattern_length // 2
    filtered_indices = []
    for idx in raw_peaks:
        if not filtered_indices or (idx - filtered_indices[-1]) > min_gap:
        filtered_indices.append(idx)

    detected_indices = np.array(filtered_indices, dtype=int) # ✅ Fix: convert to int for indexing

    # Extract detected patterns
    extracted_patterns = [filtered_packet[idx:idx + pattern_length] for idx in detected_indices]
    all_extracted_patterns.extend(extracted_patterns)
    # 🔸 Print number of patterns detected in this packet
    print(f"Packet {packet_idx + 1} - Patterns Detected: {len(extracted_patterns)}")

    # Plot correlation and detected peaks
    plt.figure(figsize=(8, 3))
    plt.plot(smoothed_correlation, label="Smoothed Cross-Correlation", color="red", alpha=0.6)
    plt.plot(adaptive_threshold, linestyle="--", color="black", label="Adaptive Threshold")
    plt.scatter(detected_indices, smoothed_correlation[detected_indices], color="blue", marker="o", label="Detected Peaks")
    plt.xlabel("Sample Index")
    plt.ylabel("Correlation Value")
    plt.legend()
    plt.title(f"Smoothed Correlation Output - Packet {packet_idx + 1} (Selection {selection})")
    plt.tight_layout()
    plt.show()

    # Plot each detected pattern's spectrogram
    for i, pattern in enumerate(extracted_patterns):
        '''
        plt.figure(figsize=(10, 4))
        plt.specgram(pattern, NFFT=256, Fs=sampling_rate, noverlap=128, scale='dB')
        plt.title(f"Spectrogram of Extracted Pattern {i + 1} (Packet {packet_idx + 1}, Selection {selection})")
        plt.xlabel("Time [s]")
        plt.ylabel("Frequency [Hz]")
        plt.colorbar(label="Power/Frequency [dB]")
        plt.tight_layout()
        plt.show()
        '''
print(f"✅ Total Patterns Detected: {len(all_extracted_patterns)}")

## Outcome
- Successfully detected and extracted signal patterns across multiple filtered packets.
- Matched filtering, adaptive thresholding, and peak detection used to localize individual bursts.
- Total number of extracted patterns: 150 in ocusyn1 data
- Total Patterns Detected: 730 in ocusync2 data
- Total Patterns Detected: 98 in ocusync3 data
- Each pattern visualized using a time-frequency spectrogram.

Low SNR Conditions
When noise overwhelms the signal, especially for small correlation peaks, adaptive thresholding may fail to distinguish actual patterns from noise.

## Step12: Moment-Based Statistical Analysis of Extracted Signal Patterns
### 🎯 Objective
To analyze the shape characteristics of extracted complex signal patterns using:
- Skewness: asymmetry of the distribution.
- Kurtosis: peakedness or flatness of the distribution.
Both are calculated from the magnitude of each complex pattern.

### 📌 Step-by-Step Description

### 🔹 1. Skewness Calculation
#### 📌 Formula (Moment-Based Skewness):

Where:
- n: number of samples in the pattern
- xi: magnitude of the i-th complex sample
- xˉ: mean of the magnitudes
- σ: standard deviation of the magnitudes
This measures asymmetry in the magnitude distribution.

### 🔹 2. Kurtosis Calculation
#### 📌 Formula (Excess Kurtosis):

Where:
- The same symbols apply as above.
- Subtracting 3 yields excess kurtosis:
### 🔹 Classification of Results: The skewness and kurtosis values were classified into categories:
  - Skewness:
    - Positive skewness indicates a longer tail to the right.
    - Negative skewness indicates a longer tail to the left.
    - Zero skewness indicates a symmetric distribution.
  - Kurtosis:
    - Leptokurtic (kurtosis > 0) indicates a sharp peak.
    - Platykurtic (kurtosis < 0) indicates a flat peak.
    - Mesokurtic (kurtosis = 0) indicates a normal distribution.

### 🔹 4. Pattern-wise Processing
For each extracted pattern:
- Compute skewness and kurtosis
- Print result with classification label
- Store values for batch analysis

### 🔹 5. Visualization with KDE
Use Kernel Density Estimation (KDE) to visualize the amplitude distributions of all extracted patterns:
- Smooth representation of signal distribution
- Helps verify assumptions about distribution shape
## 💻 Python Code
import numpy as np
import matplotlib.pyplot as plt
import seaborn as sns

# ---------- Statistical Moment Calculations ----------

def moment_based_skew(distribution):
    magnitude = np.abs(distribution)
    n = len(magnitude)
    mean = np.mean(magnitude)
    std = np.std(magnitude)
    return 0 if std == 0 else (n / ((n - 1) * (n - 2))) * np.sum(((magnitude - mean) / std) ** 3)

def moment_based_kurtosis(distribution):
    magnitude = np.abs(distribution)
    n = len(magnitude)
    mean = np.mean(magnitude)
    std = np.std(magnitude)
    return 0 if std == 0 else (1 / n) * np.sum(((magnitude - mean) / std) ** 4) - 3

# ---------- Classification Helpers ----------

def classify_skewness(skew_value):
    if skew_value > 0:
        return "Positive Skewness"
    elif skew_value < 0:
        return "Negative Skewness"
    return "Symmetrical Distribution"

def classify_kurtosis(kurt_value):
    if kurt_value > 0:
        return "Leptokurtic (Sharp peak)"
    elif kurt_value < 0:
        return "Platykurtic (Flat peak)"
    return "Mesokurtic (Normal peak)"

# ---------- Pattern Analysis Core ----------

def analyze_extracted_patterns(all_patterns):
    if not all_patterns:
        print("No patterns to analyze.")
        return

    print(f"\n📊 Total Extracted Patterns: {len(all_patterns)}\n")

    skewness_values = []
    kurtosis_values = []

    for idx, pattern in enumerate(all_patterns, 1):
        skew_val = moment_based_skew(pattern)
        kurt_val = moment_based_kurtosis(pattern)

        skewness_values.append(skew_val)
        kurtosis_values.append(kurt_val)

        print(f"📈 Pattern {idx}:")
        print(f" • Skewness: {skew_val:.4f} → {classify_skewness(skew_val)}")
        print(f" • Kurtosis: {kurt_val:.4f} → {classify_kurtosis(kurt_val)}\n")

    # ---------- KDE Plot ----------
    plt.figure(figsize=(10, 4))
    for i, pattern in enumerate(all_patterns):
        sns.kdeplot(np.abs(pattern), fill=True, alpha=0.4, linewidth=1)

    plt.title("KDE Plot of All Extracted Patterns")
    plt.xlabel("Amplitude")
    plt.ylabel("Density")
    plt.tight_layout()
    plt.show()

# ---------- Main Execution ----------

if __name__ == "__main__":
    try:
        analyze_extracted_patterns(all_extracted_patterns)
    except NameError:
        print("⚠️ Variable `all_extracted_patterns` not found. Ensure patterns are detected before running this.")

output:
Total Extracted Patterns: 150
📈 Pattern 1: • Skewness: -0.1678 → Negative Skewness • Kurtosis: -0.6948 → Platykurtic (Flat peak)
📈 Pattern 2: • Skewness: -0.2409 → Negative Skewness • Kurtosis: -0.2060 → Platykurtic (Flat peak)
📈 Pattern 3: • Skewness: -0.2376 → Negative Skewness • Kurtosis: -0.1681 → Platykurtic (Flat peak)
📈 Pattern 4: • Skewness: -0.2539 → Negative Skewness • Kurtosis: -0.1505 → Platykurtic (Flat peak)
 📈 Pattern 5: • Skewness: -0.3152 → Negative Skewness • Kurtosis: -0.1423 → Platykurtic (Flat peak)
📈 Pattern 6: • Skewness: -0.2627 → Negative Skewness
...
📈 Pattern 150: • Skewness: -0.2561 → Negative Skewness • Kurtosis: -0.0892 → Platykurtic (Flat peak)

for ocusync2 data:
📊 Total Extracted Patterns: 730
📈 Pattern 1: • Skewness: -0.9546 → Negative Skewness • Kurtosis: 3.6578 → Leptokurtic (Sharp peak)
📈 Pattern 2: • Skewness: -0.7282 → Negative Skewness • Kurtosis: 3.2478 → Leptokurtic (Sharp peak)
📈 Pattern 3: • Skewness: -1.0354 → Negative Skewness • Kurtosis: 3.9153 → Leptokurtic (Sharp peak)
📈 Pattern 4: • Skewness: -0.9132 → Negative Skewness • Kurtosis: 3.7049 → Leptokurtic (Sharp peak)
📈 Pattern 5: • Skewness: -0.4682 → Negative Skewness • Kurtosis: 8.0929 → Leptokurtic (Sharp peak)
📈 Pattern 6: • Skewness: -0.6303 → Negative Skewness
...
📈 Pattern 730: • Skewness: -1.0049 → Negative Skewness • Kurtosis: 4.1854 → Leptokurtic (Sharp peak)

For ocusunc3 data
📊 Total Extracted Patterns: 98
📈 Pattern 1: • Skewness: -0.4026 → Negative Skewness • Kurtosis: -0.2109 → Platykurtic (Flat peak)
📈 Pattern 2: • Skewness: -0.7012 → Negative Skewness • Kurtosis: 0.1434 → Leptokurtic (Sharp peak)
📈 Pattern 3: • Skewness: -0.4031 → Negative Skewness • Kurtosis: -0.2586 → Platykurtic (Flat peak)
📈 Pattern 4: • Skewness: -0.3938 → Negative Skewness • Kurtosis: -0.2531 → Platykurtic (Flat peak)
📈 Pattern 5: • Skewness: -0.3955 → Negative Skewness • Kurtosis: -0.2491 → Platykurtic (Flat peak)
 📈 Pattern 6: • Skewness: -0.4054 → Negative Skewness
...
📈 Pattern 98: • Skewness: -0.4960 → Negative Skewness • Kurtosis: -0.0520 → Platykurtic (Flat peak)